## Slide 1: Accelerated edge computing for Neural Networks
Ghent Technology Campus
2019-2020
The deployment of self-driving vehicles is one of many new and interesting low-latency applications. To aid to lower latency during localization in position fixing, a benchmark is proposed to examine the potential of executing a trained Neural Networks (NN) or Machine Learning (ML) algorithm on edge devices like the Nvidia Jetson Nano, Google Coral Dev and Raspberry Pi 3 compared to regular computer.
Introduction
In order to achieve a representative benchmark, it is necessary to investigate the performance of different programs on each edge device in an identical manner. In this benchmark several different programs are tested spread across categories of NN as regression and classification. For each program the duration of execution and utilization of the processor unit is measured and stored. To achieve statistically results, every program will be run for 20 different iterations.
Data extraction
The results show that non-edge devices remain superior compared to edge-devices. Among edge-devices, the Jetson Nano is the SBC with the lowest latency and price and thus an excellent choice for low-latency applications.
Conclusion
Student: Arno Plaetinck
Promotor: Prof. Dr. Ir. Nobby Stevens
Co-promotors: Ing. Willem Raes
Ing. Jorik De Bruycker
Master in Electronics and ICT Engineering
Technology option Embedded Systems
Academic year: 2019-2020
Date: 6/04/2020
To compare the performance of different edge devices, latency data will be adjusted for variables like processor usage, clock speed, price and energy usage. The results are normalised to ease a comparison.
Data analysis
KU Leuven
Ghent Technology Campus Gebroeders de Smetstraat 1
9000 Ghent
Program setup
Start measurement
Run NN
End measurement
iterations +1
#iterations = 20?
Next program
No
Yes